IP Module User’s Manual

Table of Contents

1	General Introduction	5

1.1	Overview	5

1.2	Feature	5

2	Module Introduction	7

2.1	With Port	7

2.1.1	Structure Dimension	7

2.1.2	Port Introduction	7

2.2	Without Port	11

2.2.1	Structure Dimension	11

2.2.2	Port Introduction	12

3	Network Connection	15

3.1	IP Module with Port in 3G	15

3.2	IP Module with Port in WiFi and Cable Network	15

4	Auto Search IP Tool	16

5	Web Operation	18

5.1	Overview	18

5.2	Login	18

6	Appendix 1 Technical Specification	21

7	Appendix 2 Factory Default Setup	23

Welcome

This user’s manual is designed to be a reference tool for the installation and operation of your system.

Here you can find information about this series IP module’s features and functions.

Before installation and operation please read the following safeguards and warnings carefully!

Important Safeguards and Warnings

1．Electrical safety

All installation and operation here should conform to your local electrical safety codes.

We assume no liability or responsibility for all the fires or electrical shock caused by improper handling or installation.

We are not liable for any problems caused by unauthorized modifications or attempted repair.

2．Installation

Do not apply power to the IP module before completing installation.

Do not put object on the IP module.

3．Environment

This series IP module should be installed in a cool, dry place away from direct sunlight, inflammable, explosive substances and etc.

- About Accessories

Be sure to use all the accessories recommended by manufacturer.

Contact your local retailer ASAP if something is missing in the accessory package.

| Name | Module with port | Module without port | Amount |
| --- | --- | --- | --- |
| IP module | ■ | ■ | 1 |
| Product warranty card | ■ | ■ | 1 |
| Certificate Card | ■ | ■ | 1 |
| User’ manual | ■ | ■ | 1 |
| Resource CD | ■ | ■ | 1 |

# General Introduction

## Overview

IP module is a medium product to be developed to either NVS or IPC. It has two types: with or without port. Multiple-port design extends the product expansibility and compatibility. You can use the module (with port), the mould from the third party and corresponding software to assemble a network video server. Or you can use the module (without port), the mould from the third party and the corresponding cable, port and software to assemble an IPC.

This series product supports D1 and CIF dual stream output. It supports PoE and WiFi and can be developed to support mobile communication data transmission module.

The various shapes, powerful performance, high and convenient expansibility make it become favorable among installer, integrator, and analog camera manufacturer.

## Feature

Please refer to the following sheet for detailed information.

| User Management | Different user rights for each group, one user belongs to one group. |
| --- | --- |
| Data Transmission | External USB port supports TD-SCDMA、EVDO（CDMA2000 1X）、WCDMA so that IP module can support mobile communication data transmission. Built-in USB port support Wifi module so that the IP module can support the wireless data transmission. Support cable network data transmission via Ethernet |
| Storage Function | Support central server backup function in accordance with your configuration and setup in alarm or schedule setting Support record via Web and the recorded file are storage in the local PC. Support local hot swap and Micro SD card memory backup function, support short time backup when encounter network connection failure. SD card and Micro SD card can storage video and image at the same time. Support FTP to transfer recorded file or image. |
| Alarm Function | Real-time respond to external alarm input( within 200MS) as user pre-defined activation setup and exert corresponding message in screen and audio prompt(allow user to pre-record audio file) Provide central management server management option so that system can initiatively send alarm notice remotely. Alarm input can connect to various peripheral equipments. Provide prompt or alarm option when encounter video loss. Support SMS(short messaging service) function when alarm occurs. |
| Network Monitor | IP module support one-channel audio/video data transmit to network terminal and then decode. Delay is within 500ms (network bandwidth support needed) Max supports 10 connections. Adopt the following audio and video transmission protocol: HTTP, TCP, UDP, and MULTICAST. Send some alarm data or message via SMTP. Support web access, used in WAN. |
| Network Management | Realize IP Module configuration and management via Ethernet. Support device management via web. |
| Peripheral Equipment | Support peripheral equipment management, each peripheral equipment control protocol and interface can be set freely. Support serial port (RS232/RS485) transparent data transmission. Support PoE. |
| Assistant Function | Support system resource information and running status real-time display. Video format support NTSC and PAL. Support log function. Support video watermark function to avoid vicious video modification. Use IR receiver to receive the IR signal. |

# Module Introduction

## With Port

### Structure Dimension

Please refer to the following two figures for detailed information.

Figure 2-1

Figure 2-2

### Port Introduction

Please refer to the following figures for port information.

Figure 2-3

Please refer to the following sheets for detail information.

| Indication light /Port | Function | Color/Port Type | Note |
| --- | --- | --- | --- |
| Red/green light | Power/working status indication light | Red/green | When connect the IP module to the power：Red light is on. When device is working normally：Green light is on. When device is upgrading：The green light is flashing. Device is off or there is no power: The indication light becomes off. |
| Red light | Alarm status indication light | Red | Device has been armed：The light is on. There is data transmission：The light is flashing. Device has been disarmed：The indication light is off. |
| Green light | Wireless network status indication light | Green | Wireless network connection is OK：The light is on. Wireless network connection is abnormal：The light is off. |
| Yellow light | Video transmission/record status indication light | Yellow | Video transmission is OK：The light is on. Video transmission is abnormal：The light is flashing. |
| Video input port |  | BNC port | Input analog video signal. It can connect to the devices such as camera. |
| Video output port |  | BNC port | Output analog video signal. It can connect to the devices such as the displayer. |
| Video input port | LINE IN | 3.5mm JACK port | Input analog audio signal. It can connect to the devices such as active microphone. |
| Audio output port | LINE OUT | 3.5mm JACK port | Output analog audio signal. It can connect to the devices such as the sound box. |
| External USB port/ External TD port |  |  | USB port. It can be extended to the external TD port. |
| IR remote port |  |  | It is to receive the IR remote signal to control GUI menu. |
| Built-in POE port |  |  | 24pin--built-in PoE port to connect to the PoE module. |

Figure 2-4

Note:

I/O port pin from the right to left are: A/B/1/2/NO/C/RX/TX/G port.

Please refer to the following sheet for detailed information.

| Port | Function | Color | Note |
| --- | --- | --- | --- |
| G | GND | I/O port | Ground end |
| TX |  |  | RS232_TX，RS232 COM sending end. |
| RX | Transparent debug COM |  | RS232_RX，RS232 COM receiving end. |
| C | 1 channel alarm output |  | Alarm output port. It is to send out alarm signal to the alarm device. C：Alarm output public end. NO：NO alarm output end. |
| NO |  |  |  |
| 2 | 1-2ch alarm input |  | Alarm input port1: It is to receive external alarm source signal. |
| 1 |  |  | Alarm input port 2: It is to receive external alarm source signal. |
| B | RS485 port |  | RS485_B port， control external PTZ. |
| A |  |  | RS485_A port， control external PTZ |
| SD card port |  |  | Connect to the SD card. |
| RESET Button |  |  | It is a device reset button. Press it for at least five seconds to reboot system to restore factory default setup. |
| Power Port |  |  | Connect to power DC 12V or AC 24V. |
| Network Port |  |  | Connect to the network cable |

Figure 2-5

Please refer to the following sheet for detailed information.

| Pin No. | Pin Name | Note |
| --- | --- | --- |
| 1 | +3.3V_AUDIO | It can provide power to amplifier MIC, MAX=50mA |
| 2 | MIC IN |  |
| 3 | GND |  |

Figure 2-6

## Without Port

### Structure Dimension

Please refer to the following sheet for detailed information.

Figure 2-7

Figure 2-8

Figure 2-9

### Port Introduction

Please refer to the following figures for port information.

Figure 2-10

Figure 2-11

2-pin 12VDC power output port (IR receiver)

| PIN No. | Name | Note |
| --- | --- | --- |
| 1 | Earthed |  |
| 2 | +12V | Output power is defined by external +12V power Current is below 300mA. |

4-pin video input port.

| PIN No. | Name | Note |
| --- | --- | --- |
| 1 | +12V | Provide power to front-end camera. Output power is defined by external +12V power. |
| 2 | Earthed |  |
| 3 | VIDEO_IN |  |
| 4 | Earthed |  |

3-pin MIC input port

| PIN No. | Name | Note |
| --- | --- | --- |
| 1 | +3.3V_AUDIO | It can provide power to the MIC of built-in amplifier. MAX power=50mA. |
| 2 | MIC IN |  |
| 3 | Earthed |  |

30-pin user Interface

| PIN No. | Name | Note |
| --- | --- | --- |
| 1 | NET_LED_LINK | Network connection indication light. It becomes active when it is high. It can directly drive LED light. |
| 2 | NET_LED_ACT | Network connection indication light. It becomes active when it is high. It can directly drive LED light. |
| 3 | ETHRX- | Network signal |
| 4 | ETHRX- |  |
| 5 | ETHRX+ |  |
| 6 | ETHRX+ |  |
| 7 | GPIO16_PRESET | Restore system default setup. It becomes active when it is low. It hangs when it is invalid. |
| 8 | POWER_LED | Power indication light. It can directly drive LED light. |
| 9 | Earthed | Signal earthed. |
| 10 | Earthed |  |
| 11 | ALARM_IN2 | Alarm input 2. It becomes active when it is low. It hangs when it is invalid. |
| 12 | GND_EARTH0 | Network earthed It can hang. |
| 13 | RS485_A | 485 signal |
| 14 | GND2_POE | For PoE . It connects to PIN7 and PIN8 of RJ45. |
| 15 | RS485_B | 485 signal |
| 16 | +48_IN2 | For PoE . It connects to PIN4 and PIN5 of RJ45. |
| 17 | ALARM_COM | Alarm output. Two signals constitute the alarm output button. Max value 1A @30VDC or 0.3A @125VAC when button is on. |
| 18 | ALARM_NO |  |
| 19 | +12V_DC | User power input 12VDC |
| 20 | +12V_DC |  |
| 21 | GND_12 | User power output earthed |
| 22 | GND_12 |  |
| 23 | RX0 | Debug COM input |
| 24 | ALARM_IN1 | Alarm input1. It becomes active when it is low. Connect to 5V or hangs when it is invalid. |
| 25 | TX0 | Debug COM output. |
| 26 | AUDIO_OUT | Audio output. 1-ch |
| 27 | Earthed | Signal earthed. |
| 28 | AUDIO_IN | Audio input. 1-ch |
| 29 | VIDEO_OUT | Analog video output |
| 30 | Earthed | Signal earthed |

# Network Connection

## IP Module with Port in 3G

Please refer to the following sheet for detailed information.

Figure 3-1

## IP Module with Port in WiFi and Cable Network

Please refer to the following sheet for detailed information.

Figure 3-2

# Auto Search IP Tool

Auto search IP tool allows you to search or modify IP module current IP address.

Open AutoSearchDevc.exe (), click device list item you can an interface is shown as in Figure 4-1. Here you can view device IP address, port, sub-net mask and gateway information.

Figure 4-1

In Figure 4-1, double click one IP address you can see a web interface. See Figure 4-2.

Figure 4-2

In Figure 4-1, select one IP and then click “modify” button, you can see an interface is shown as in Figure 4-3. You can input device user name and address and then log in.

Figure 4-3

After you logged in, you can see an interface is shown as in Figure 4-4. Here you can modify device IP address, sub-net mask and gateway information.

Figure 4-4

# Web Operation

## Overview

IP module support Web access via PC to manage device.

Web operation consists of the following operation sections: monitor channel, record search, alarm setup, system setup, PTZ control and monitor window.

## Login

Before web operation, please check the following items:

- PC and IP module connection is OK.

- You have set PC IP address, IP module IP address, subnet mask and gateway. (Please set the IP address of the same section for the PC and IP module. Please input corresponding gateway and subnet mask if there are routers.) IP module default IP address is 192.168.1.108.

- Use order ping ***.***.***.***(IP module IP address) to check connection is OK or not. Usually the return TTL value should be less than 255.

Open IE and input IPC IP address in the address column. For example, if your IP module IP is 192.168.1.108(factory default IP address), then please input http:// 192.168.1.108 in IE address column. See Figure 5-1.

Figure 5-1

System pops up warning information to ask you whether install webrec.cab control or not. Please click yes button.

If you can’t download the ActiveX file, please modify your settings as follows. See Figure 5-2.

Figure 5-2

After installation, the interface is shown as below. See Figure 5-3.

Please input your user name and password.

Default factory name is admin and password is admin.

Note: For security reasons, please modify your password after you first login.

Figure 5-3

After you logged in, you can see the main window.  See Figure 5-4.

There are six sections:

- Section 1: Monitor channel menu tree

- Section 2:  System menu

- Section3: PTZ control

- Section4: Color setup and other setup

- Section5: Preview window

- Section 6: Monitor window switch

Figure 5-4

Please refer to the Web operation manual included in the resource CD for detailed information.

# Appendix 1 Technical Specification

| Parameter | Specification |
| --- | --- |
|  | With Port | Without Port |
| System Resources | Max supports 10 network users to log in and operate. |
| OS | Embedded Linux real-time OS. |
| Operation Interface | WEB |
| Video Resolution | Real-time PAL/NTSC. Support D1/HD1/CIF/QCIF/QVGA/QQVGA. |
| Video Compression | H.264 CBR and H.264 VBR |
| Bit Stream Control Mode | CBR/VBR |
| Frame Rate Control | ACF-Active Control Frame |
| Motion Detection | Zone setup：PAL：396(22*18) ，NTSC：330(22*15). Motion detection sensitivity:1-6 level for each zone. |
| Audio Compression Standard | G.711／AMR |
| Video Format | PAL（625Line，50f/s），NTSC（525Line，60f/s） |
| Video Input | 1-ch analog video input. BNC port. Level； 1.0Vp-p. Resistance：75Ω |
| Video Output | 1-channel analog video output. BNC port. Level； 1.0Vp-p. Resistance：75Ω | / |
| Audi o Input | 1-channel audio talk input, 3.5mm JACK LINE IN. |
| Audio Output | 1-channel audio talk output 3.5mm JACK LINE OUT. | / |
| Frame Rate | Real-time mode： NTSC 1f/s-30f/s for each channel (Adjustable). PAL 1f/s-25f/s for each channel (Adjustable) |
| Video Quality | 1-6 level |
| Alarm Input | 2-ch alarm input | / |
| Alarm Output | 1-ch relay output. Relay （DC 30V 1A，AC 125V 0.5A（Activation output）） | / |
| Wlan | Working area: 100m (no obstacle) WLAN antenna parameter: Gain: 3db. Resistance: 50Ω |
| Clock | Built-in real-time clock |
| Indication Light | One power/working status indication light. One video transmission/record indication light. One alarm indication light. One wireless network indication light. | / |
| RS232 | One RS232 port to debug transparent COM data. | / |
| RS485 | One RS485 port to control PTZ. Support various protocols. | / |
| IR Remote Port | / | 1 IR remote signal port |
| Storage Card Port | SD card port | Micro SD card port |
| External USB Port | TD port/EVDO port can connect to TD-SCDMA2000 device, EVDO module. | / |
| Built-in USB port | WiFi module port can connect to WiFi module | / |
| Network Port | RJ45 10M/100M self-adaptive Ethernet port | / |
| Power | Power adapter, external equipment. Input DC 12V or compatible with Dc 12V and AC 24V both. | / |
|  | PoE |
| Power Consumption | ＜5W |
| Working Temperature | 0℃～+50℃ |
| Humidity | 10℅～90℅ |
| Air pressure | 86kpa～106kpa |
| Dimension | 117mm*53mm*34mm | 63mm*58mm*14mm |
| Weight | 90g | 40g |

# Appendix 2 Factory Default Setup

| Function Configuration Type | Item Name | Default setup |
| --- | --- | --- |
| General Setup | Date format | Y-M-D |
|  | DST | Disable by default |
|  | Date separator | ‘ _ ’ |
|  | Time format | 24H |
|  | Language | Simplified Chinese |
|  | When HDD is full | Overwrite |
|  | Record duration | 60M |
|  | Device No. | 8 |
|  | Video type | PAL |
| Encode Setup | Channel | Channel01 |
|  | Encode mode | H.264 |
|  | Audio/Video enable | Enable audio and video |
|  | General bit stream | General bit stream |
|  | Resolution | D1 |
|  | Frame rate | 25 |
|  | Bit stream control | VBR |
|  | Quality | Good |
|  | Bit stream value | 1024 |
|  | I frame interval control | 50 |
|  | Video color | Brightness:50 Contrast:50 Sautratioon:50 Hue:50 |
|  | Watermark | Enable Watermark: all Watermark type: character Watermark: Digital CCTV |
|  | Privacy mask | Never |
|  | Time title | Enable. OSD transparent :128 |
|  | Channel title | Enable. OSD transparent :128 |
| Record Setup | Channel | Ch01 |
|  | Pre-record | 5 seconds. |
|  | Storage setup | Record: schedule/motion detection/alarm local storage Snapshot: schedule/motion detection/alarm, local storage |
|  | Time Setup | Start Time | 0:00:00 |
|  |  | End Time | 23:59:59 |
|  |  | Record | Enable schedule/motion detection/alarm |
|  |  | Snapshot | Enable motion detection/alarm |
|  |  | Week | Current date |
| COM Setup | Option | COM01 |
|  | Function | General |
|  | Data bit | 8 |
|  | Stop bit | 1 |
|  | Baud rate | 115200 |
|  | Parity | None |
| Network Setup | Ethernet | Port 01 |
|  | DHCP | Disable |
|  | IP address | 192.168.1.108 |
|  | Subnet mask | 255.255.0.0 |
|  | Gateway | 192.168.0.1 |
|  | Device name | Device factory default name |
|  | TCP port | 37777 |
|  | HTTP port | 80 |
|  | UDP port | 37776 |
|  | Network user connection amount | 10 |
|  | Network transmission QoS | Disable |
|  | Remote host | Multiple broadcast group |
|  | Enable | Disable |
|  | IP address | 255.255.255.0 |
|  | Port | 36666 |
|  | Email setup | Enable |
|  | Multiple DDNs | Disable |
|  | NAS setup | Disable |
|  | NTP setup | Disable |
|  | Alarm server | Disable |
| Alarm Setup | Event type | Local |
|  | Alarm input | Input 01, disable |
|  | Type | Normal open |
|  | Setup | Period: Start time 0:00:00 End time:23:59:59 Period 1:enable Week: Current week |
|  | Anti-dither | 0 second |
|  | General output | Disable |
|  | Alarm latch | 10 seconds |
|  | Record channel | 1, enable |
|  | Record latch | 10 seconds |
|  | Send email | Disable |
|  | PTZ activation | Event type: never Address: 0 |
|  | Snapshoot | Disable |
| Video Detection | Event type | Motion detection |
|  | Channel | Ch1, Disable |
|  | Sensitivity | 3 |
|  | Time period setup | Period: Start time 0:00:00 End time:23:59:59 Period 1:enable Week: Current week |
|  | Anti-dither | 5 seconds |
|  | General output | Disable |
|  | Alarm latch | 10 seconds |
|  | Record channel | Disable |
|  | Record latch | 10 seconds |
|  | Send email | Disable |
|  | PTZ activation | Event type: Never Address: 0 Disable |
|  | Snapshot | Disable |
| PTZ Setup | Channel | Ch01 |
|  | Protocol | DH-SD1 |
|  | Address | 1 |
|  | Baud rate | 115200 |
|  | Data bit | 8 |
|  | Stop bit | 1 |
|  | Parity | None |
| Default and Backup | All | Disable |
|  | General | Disable |
|  | Encode | Disable |
|  | Record | Disable |
|  | COM | Disable |
|  | Network | Disable |
|  | Alarm | Disable |
|  | Video detection | Disable |
|  | Display output | Disable |
|  | Channel No. | Disable |
| Advanced | Record control | Auto. Ch1 |
|  | Abnormity | Even Type | No HDD, disable |
|  |  | General Output | Disable |
|  |  | Alarm Latch | 10 seconds |
|  |  | Send email | Disable |
|  | User account | admin--- password: admin 888888--- password: 888888 666666--- password: 666666 default--- password: tluafed |
|  | Snapshot | Channel | Ch01 |
|  |  | Snapshot mode | Scheduled |
|  |  | Frame rate | 1f/s |
|  |  | Resolution | D1 |
|  |  | Quality | 60% |
|  | Auto maintain | Auto reboot | Never |
|  |  | Auto delete old files | Never |
| Additional Setup | Auto Registration | Enable | Disable |
|  |  | IP | 0.0.0.0 |
|  |  | Port | 7000 |
|  | DNS | DNS | 202.101.172.35 |
|  |  | Alternative DNS | 202.101.172.35 |
|  | IP Filter | Disable |
|  | Audio Talk Encode | G.711a |

Note:

- This manual is for reference only. Slight difference may be found in the user interface.

- All the designs and software here are subject to change without prior written notice.

- Please visit our website or contact your local retailer for more information.

# Text boxes

30pin-user port

2pin-12V power output port

2

1

29

30

2

1

1

3

PoE reserved port

4pin- built-in USB port

3pin-bult-in MIC

FPC/FFC port

IR remote signal receiver

Power indication light

24-pin--built-in PoE port

RESET port

⑥

⑤

②

③

①

④

Input your IP address here.

Network port

SD card port

Video output port

Video input port

Audio output port

Audio input port

External USB port

Red

Green

Yellow

I/O Port

3

1

Power port

3pin-MIC input port

4

Reserved POE port

4pin-built-in Wifi port

1

SD card port

4pin-video input port